Revised:  28JA2006

# REMOVING C2/C3 ASSIST CYLINDER SEALS & WASHERS

Through most C3 production (up through 1980) the rod scraper, scraper element, backup washer, snap ring, and hydraulic seal consisted of five distinct parts.  During 1981 production the package was revised to a one piece scraper and backup washer design.  The new design still assembled into the same cylinder end cavity.  The seal and snap ring did not change.  This change is show in another paper entitled Booster Cylinder Seal Packages available from the author or from the host websight.

Here are some ideas to assist in removing the rod seal and the backup washer from the assist (booster) cylinder (after removing the snap ring):

1).  A.  Fully extend the rod.

B.  Get a small screwdriver and bite the edge of the washer.

C.  Slowly retract the rod while biting the washer.

D.  Once it moves in relation to the rod, extend the rod and you

will be able to remove the washer.

2).  A.  Use a small screwdriver and hammer to tap the washer and

get it rotating.

B.  Extend and retract the rod until the washer comes out.

C.  Do the same thing with the seal.

3).  Use air or oil pressure to blow the washer and seal out.

The cylinder is of welded construction.  Therefore, even though the rod seals can be removed, the seal on the piston inside the cylinder is not serviceable.

AssistCylinderSealRemoval.doc

JIML82@aol.com